## Slide 1: Toward Open Source Intrusion Tolerant SCADA
Trevor Aron
JR Charles
Akshay Srivatsan
Mentor: Marco Platania

## Slide 2: Outline
What is SCADA?
SCADA Vulnerabilities
What is Intrusion Tolerance?
Prime
PvBrowser
Our Architecture
Demo
Future Directions

## Slide 3: What is SCADA?
Supervisory Control and Data Acquisition
Used to supervise and control national infrastructure
Main components:
  Master
  HMI
  PLCs/RTUs
Designed to work with propriety hardware and protocols
Components are connected on private, isolated network

## Slide 4: SCADA in Power Grids (1)
Power grids include generation plants and transmission/distribution substations which are spread across wide areas
  Electrical Generation Plant: generates electrical power to be transmitted across the grid
  Transmission Substation: transforms power for long distance transmission and provides switching between sources/destinations to meet the needs of the grid
  Distribution Substation: receives power from a transmission substation(s) to be distributed on site

## Slide 5: SCADA in Power Grids (2)
SCADA system is used to monitor power substations
RTUs read data from field devices
  Transformers
  Generators
  Switches
  …
Data is processed by the SCADA master and presented to the user through the HMI
If the values read from RTUs exceed predefined safety threshold, alarms are raised by the master

## Slide 6: SCADA Systems moving to the Internet
Traditional Security Model
  Perimeter based
  Security through obscurity
  Primary/Standby Architecture
SCADA systems originally designed to run on private networks and are not optimized for security
In the past decade, SCADA systems witnessed many changes
  Use of off-the-shelf hardware
  Standardized protocols
  Open networks (e.g. Internet)

## Slide 7: SCADA vulnerabilities
Attacks exploiting software vulnerabilities
  Stuxnet
  Project SHINE
  Attacks involving foreign governments
Current solutions are ineffective against malicious intrusions

## Slide 8: What is Intrusion Tolerance?
Intrusion Tolerance: Executing correct operations even if a part of the system is controlled by an adversary
  Safety: all correct replicas maintain consistent state
  Liveness: eventual progress
There are many algorithms in literature that provide byzantine fault tolerant replication, until less than one third of the system is compromised
  BFT
  Zyzzyva
  Prime
  Aardvark
  …

## Slide 9: Prime: Byzantine Replication with Performance Guarantees Under Attack
First BFT protocols to provide performance guarantees while under attack
Limits the power of a malicious leader to achieve bounded delay performance guarantee

## Slide 10: Defense across space and time
Prime and BFT protocols in general are fragile over long system life time
Solution
  Defense Across Space: diversify the execution environment to generate different versions of the same application
  Defense Across Time: periodic and proactive replica rejuvenation to clean undetected intrusions
  Diversity + Proactive recovery allow for long lived intrusion tolerant systems

## Slide 12: Intrusion tolerant SCADA
Use Prime to replicate SCADA masters
SCADA master works correctly if no more then f replicas out of 3f+1 replicas have been intruded
Diversity and proactive recovery allow for the system to function for a long time
An earlier version of Prime was integrated by Siemens into their SCADA product for the power grid, but it does not include diversity and proactive recovery (no protection across space and time)

## Slide 13: Our Goals
To develop a proof-of-concept of an open source intrusion tolerant SCADA
Components:
  PvBrowser: Open source SCADA software
  Prime: Intrusion tolerant replication with performance guarantees under attack
  RTU emulator: simulates data generation from field devices

## Slide 14: PvBrowser
Open source SCADA Master and HMI server
Architecture
  Master
    Data acquisition daemon (DAD): communicates with RTUs/PLCs
    Shared memory: medium for communication between DAD and Pvserver
    ProcessViewServer: visualizes data from DAD and communicates with HMI
  HMI
    ProcessViewBrowser: presents information from the visualizer to user

## Slide 15: PvBrowser (Modifications)

## Slide 16: PvBrowser (Modifications)
Break Shared Memory

## Slide 17: PvBrowser (Modifications)
Break Shared Memory
Implement message passing between DAD and PVServer
Allows us to:
  Eliminate nondeterministic behavior

## Slide 18: PvBrowser (Modifications)
Break Shared Memory
Implement message passing between DAD and PVServer
Allows us to:
  Eliminate nondeterministic behavior
  Run processes on different machines

## Slide 19: PvBrowser (Modifications)
Break Shared Memory
Implement message passing between DAD and PVServer
Allows us to:
  Eliminate nondeterministic behavior
  Run processes on different machines
  Implement replication

## Slide 20: Modbus
Standardized communication protocol used by many SCADA systems around the globe
Used to communicate with Remote Terminal Units (RTUs)
Values stored in memory registers, organized as:
  Input Registers: analog inputs of different types (e.g. voltage, amperage)
  Input Status: digital input used to represent dichotomous values (e.g. electrical breakers, switches)
  Coil Status: digital output used to switch voltage in a relay (e.g. switch power ON/OFF to field device)
  Holding Registers: store additional data the can be used by other devices; less commonly used

## Slide 21: Modbus Example

## Slide 22: Our Architecture
DAD and 3f+1 PVServers all run on different physical machines
DAD polls RTUs and communicates data to servers via message passing
Data polled from field units is replicated consistently across all servers using Prime
HMI can connect to any server and observe consistent data at each correct replica
BROWSER
MASTER
MASTER
MASTER
MASTER
Data Acquisition
PRIME
RTU
RTU
RTU
MODBUS

## Slide 23: RTU Emulator
ASE2000 Version 2 RTU Test Set
Allows the user to define RTUs
For each RTU, it is possible to specify communication protocol (e.g. Modbus) and the number of registers
Used to test how the SCADA master responds to events (e.g. change of values/states)
Allows testing of newly implemented protocols (e.g. DNP3)

## Slide 24: RTU Emulator Example

## Slide 25
https://cdn.fbsbx.com/hphotos-xap1/v/t59.2708-21/11170697_10206615424567947_1652314067_n.pdf/PowerGridOverview-Dagle.pdf?oh=a311fd53c7bdbe0459294bafa930067f&oe=5547523F&dl=1

## Slide 26: Future Directions
Our Architecture provides intrusion tolerant replication of the data used by the SCADA Master
BROWSER
MASTER
MASTER
MASTER
MASTER
Data Acquisition
PRIME
RTU
RTU
RTU
MODBUS

## Slide 27: Future Directions
Our Architecture provides intrusion tolerant replication of the data used by the SCADA Master
Additional components:
  Replication of all events involving the SCADA master, allowing a client to compare the state of each server and determine the correct state (with f+1 consistency)
BROWSER
MASTER
MASTER
MASTER
MASTER
Data Acquisition
PRIME
RTU
RTU
RTU
MODBUS
CLIENT LIBRARY

## Slide 28: Future Directions
Our Architecture provides intrusion tolerant replication of the data used by the SCADA Master
Additional components:
  Replication of all events involving the SCADA master, allowing a client to compare the state of each server and determine the correct state (with f+1 consistency)
  Implementing intrusion tolerance for data acquisition
    Replicating DAD
    Using Prime to synchronize and order data polled from RTUs/PLCs
BROWSER
MASTER
MASTER
MASTER
MASTER
Data Acquisition
PRIME
RTU
RTU
RTU
MODBUS
CLIENT LIBRARY
Data Acquisition
Data Acquisition
Data Acquisition

## Slide 29: Special Thanks
Johns Hopkins DSN Lab
Dr. Yair Amir
Dr. Marco Platania

## Slide 30
Critical Infrastructures (power grids, water plants, transportation systems, …) are at the heart of human society
Power grids are particularly important because other Critical Infrastructures, systems, and human activities rely on them
This is one of the factors that make power grids an increasingly important target for cyber attacks
  In 2013 DHS reported that in 2012 the 40% of cyber attacks targeted the energy sector
“Now our enemies are also seeking the ability to sabotage our power grid, our financial institutions, and our air traffic control systems. We cannot look back years from now and wonder why we did nothing in the face of real threats to our security and our economy”
Barack Obama, State of the Union 2013
Intrusion tolerance: the time is now!

## Slide 31
Breaking the barriers
Power service industry is highly regulated
Power companies strictly follows the regulation requirements
SCADA system manufacturers have no (or little) incentive to develop capabilities that are not demanded by power companies
Because intrusion tolerance is not on the regulations, power companies and SCADA system manufacturers are not interested in working on intrusion tolerant solutions
The first prototype of intrusion tolerant SCADA produced by Siemens was never translated to a product in the field, lacking customer demand and regulatory requirements

## Slide 32
Our goal
Building the first survivable intrusion tolerant open source SCADA system
Impact on the energy ecosystem:
  Showing to regulators, power companies, and SCADA manufacturers the importance of intrusion tolerance and that the problem is solvable
  Making intrusion tolerant a regulatory requirement
  Showing and teaching SCADA manufacturers how to integrate intrusion tolerance in their own systems via open source
  Involving other researchers so to enlarge the SCADA community and increase the impact that it can have