## Slide 1: Small Form Computing
A bump in the wire

## Slide 2: The questions
What can we do with an inexpensive small computer?
Can we make it a part of a seamless wireless mesh network by installing SMesh?
Can we make it a robot controller by performing computations on it?
Can it encrypt/decrypt? At what rate?

## Slide 3: The answers
Let’s try and run something on it
Learn about its target platform
  MIPS 32 architecture
  Single Core
  Little Endian
  Memory – 61 MB
What about its capability?
  Need of standard benchmarks

## Slide 4: Linux to the rescue - OpenWRT
A Linux distribution for embedded devices
Flash the router!
Bleeding edge version - Chaos Calmer

## Slide 5: Now the benchmarking ..
File Transfer over TCP
  Wired: 89 Mpbs Wireless: 44 Mpbs With I/O: 7Mbps
OpenSSL benchmarks
Definitely not for Asymmetric Encryption!
Test ( for 3 seconds) block size: 16 | Cloud2 Bps | NEXX Bps
SHA1 | 31787.25K | 2805.40K
AES 256 CBC | 54005.82K | 6222.59K
2048 bit private RSA for 10s | 1384 signs/s 49705 verify/s | 8.1 signs/s 257.9 verify/s

## Slide 6: Let’s write some code…
Cross compilation – Sourcery codebench Lite, OpenWRT SDK
mipslinux-gnu-gcc -msoft-float -EL -static <helloworld.c> -o <helloworld>
Get USB support - opkg package manager
Building a simple package using the SDK

## Slide 7: What do we do with it?
What about a Bump-In-The-Wire?
Set it up as two intermediary hops between two hosts trying to communicate
Encryption/Decryption on the fly

## Slide 8: Topology
(LAN: 192.168.3.1)
NEXX 2
(WAN: 192.168.4.1)
Host 1
192.168.3.222
Host 2
192.168.1.128
(LAN: 192.168.1.1)
NEXX 2
(WAN: 192.168.4.3)
ICMP
Sends a ping request
XXXX
Sends a ping reply
Encrypts/Decrypts
Decrypts/Encrypts
ICMP

## Slide 9: Step 1
Understanding Journey of an IP packet through the network

## Slide 10: All that jargon
Checksums
Sniffing
Netfilter
Raw sockets
IPTables
Packet Capture

## Slide 11: Raw Sockets
A user level application can open a raw socket to get packets exactly as they would arrive on the network
Not suitable for this application - creates a ‘clone’ of each incoming packet for every application that has opened a raw socket, to listen to that type of packet. It didn’t really ‘bypass’ the kernel processing

## Slide 12: Divert Sockets
They fit the bill, their very use case was to filter specific packets and get them to user space, giving the process total control of the packet. It could pass the packet as is, or choose to mangle it
IPPROTO_DIVERT – instruct the firewall to send packets to a certain port, to which this socket is bound
Different kernel needed

## Slide 13: Netfilter/Iptables
A framework for packet filtering, a kernel subsystem in all modern linux kernels, all incoming packets traverse the netfilter subsystem
Iptables - a user level application to interact with netfilter modules

## Slide 14: Digging into Netfilter
Each protocol (IPV4/IPV6/DECnet )defines ‘hooks’. These are well defined points in a packet’s traversal of that protocol stack
Kernel modules can register to listen on different hooks of that stack with priority. Packets are passed to them in order of priority on arrival
These modules, can decide the ‘fate’ of the packet
  NF_DROP/NF_ACCEPT/NF_STOLEN/NF_QUEUE
Packets that are queued, are handled in user space

## Slide 15: Packet Traversing Netfilter system
NF_IP_PRE_ROUTING
ROUTE
NF_IP_FORWARD
NF_IP_POST
NF_IP_LOCAL
ROUTE
NF_IP_LOCAL_OUT

## Slide 16: Iptables
A packet selection system that is built over Netfilter
The ‘tables’ are modules that are registered at various ‘hooks’ in this framework, these ‘hooks’ are referred to as ‘chains’ when handling incoming packets
Iptables –t mangle –I FORWARD –p tcp –j ACCEPT
Iptables –t mangle –I FORWARD –p tcp –j NF_QUEUE

## Slide 17: Libnetfilter queue
Userspace library providing an API to packets that have been queued by the kernel packet filter
Three step process:
Library setup – nfq_open(), nfq_unbind_pf(), nfq_bind_pf()
Message receiving – callback function for each received packet
Exit phase – nfq_close()

## Slide 18: Our system
Packet received – call back function – check type – encrypt/decrypt – re-calculate checksums – issue verdict
Queue 0
Queue 1
nfqnl_program
From LAN
From WAN
Processed packet

## Slide 19: Encryption / Decryption
Using simple XOR
AES Encryption
OpenSSL library

## Slide 20: Performance (all wired)
Tool / Method | XOR | AES | No queue
PING packets | 2 ms | 2.2 ms | 1 ms
Iperf (TCP) | 15.7 Mbps | 11 Mbps | 94 Mbps
File Transfer (TCP) ( 20 MB ) | 13.54 Mbps | 8.8 Mbps | 90 Mbps

## Slide 21: Conclusions
For performance improvement, write a netfilter hook ( loadable kernel module) instead of mangling packets in user space – will need to see how encryption can be done here
How does this perform encryption with respect to other tools
Is this value for money?

## Slide 22: References
http://sock-raw.org/papers/sock_raw
https://home.regit.org/netfilter-en/using-nfqueue-and-libnetfilter_queue/
http://www.netfilter.org/projects/iptables/index.html

## Slide 23: Questions ?
Thank you!